## Slide 1: Design of Digital Circuits Lecture 17b: Branch Prediction I
Prof. Onur Mutlu
ETH Zurich
Spring 2019
18 April 2019

## Slide 2: Required Readings
This week
  Smith and Sohi, “The Microarchitecture of Superscalar Processors,” Proceedings of the IEEE, 1995
  H&H Chapters 7.8 and 7.9
  McFarling, “Combining Branch Predictors,” DEC WRL Technical Report, 1993.

## Slide 3: Agenda for Today & Next Few Lectures
Single-cycle Microarchitectures
Multi-cycle and Microprogrammed Microarchitectures
Pipelining
Issues in Pipelining: Control & Data Dependence Handling, State Maintenance and Recovery, …
Out-of-Order Execution
Other Execution Paradigms

## Slide 4: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 5: Control Dependence Handling

## Slide 6: Control Dependence
Question: What should the fetch PC be in the next cycle?
Answer: The address of the next instruction
  All instructions are control dependent on previous ones. Why?
If the fetched instruction is a non-control-flow instruction:
  Next Fetch PC is the address of the next-sequential instruction
  Easy to determine if we know the size of the fetched instruction
If the instruction that is fetched is a control-flow instruction:
  How do we determine the next Fetch PC?
In fact, how do we even know whether or not the fetched instruction is a control-flow instruction?

## Slide 7: Branch Types
Type | Direction at fetch time | Number of possible next fetch addresses? | When is next fetch address resolved?
Conditional | Unknown | 2 | Execution (register dependent)
Unconditional | Always taken | 1 | Decode (PC + offset)
Call | Always taken | 1 | Decode (PC + offset)
Return | Always taken | Many | Execution (register dependent)
Indirect | Always taken | Many | Execution (register dependent)
Different branch types can be handled differently

## Slide 8: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions.
Potential solutions if the instruction is a control-flow instruction:
Stall the pipeline until we know the next fetch address
Guess the next fetch address (branch prediction)
Employ delayed branching (branch delay slot)
Do something else (fine-grained multithreading)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 9: Stall Fetch Until Next PC is Known: Good Idea?
IF
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
IF
IF
IF
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
IF
IF
IF
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
IF
MEM
ID
IF
IF
IF
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
IF
MEM
ID
IF
WB
ALU
IF
IF
IF
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
IF
MEM
ID
IF
WB
ALU
IF
MEM
ID
IF
IF
IF
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
IF
MEM
ID
IF
WB
ALU
IF
MEM
ID
IF
WB
ALU
IF
IF
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
This is the case with non-control-flow and unconditional br instructions!

## Slide 10: The Branch Problem
Control flow instructions (branches) are frequent
  15-25% of all instructions
Problem: Next fetch address after a control-flow instruction is not determined after N cycles in a pipelined processor
  N cycles: (minimum) branch resolution latency
If we are fetching W instructions per cycle (i.e., if the pipeline is W wide)
  A branch misprediction leads to N x W wasted instruction slots

## Slide 11: Importance of The Branch Problem
Assume N = 20 (20 pipe stages), W = 5 (5 wide fetch)
  Assume: 1 out of 5 instructions is a branch
  Assume: Each 5 instruction-block ends with a branch
How long does it take to fetch 500 instructions?
  100% accuracy
    100 cycles (all instructions fetched on the correct path)
    No wasted work; IPC = 500/100
  99% accuracy
    100 (correct path) + 20 * 1 (wrong path) = 120 cycles
    20% extra instructions fetched; IPC = 500/120
  90% accuracy
    100 (correct path) + 20 * 10 (wrong path) = 300 cycles
    200% extra instructions fetched; IPC = 500/300
  60% accuracy
    100 (correct path) + 20 * 40 (wrong path) = 900 cycles
    800% extra instructions fetched; IPC = 500/900

## Slide 12: Branch Prediction

## Slide 13: Branch Prediction: Guess the Next Instruction to Fetch
0x0004
0x0005
0x0006
0x0007
0x0008
I-$
RF
LD R1, MEM[R0]
ADD R2, R2, #1
0x0001
BRZERO 0x0001
0x0002
0x0003
DEC
ADD R3, R2, #1
0x0004
LD R2, MEM[R2]
MUL R1, R2, R3
0x0005
0x0006
LD R0, MEM[R2]
0x0007
12 cycles
8 cycles
D-$
PC
??
Branch prediction
WB
Stall fetch

## Slide 14: Misprediction Penalty
LD R0, MEM[R2]
LD R2, MEM[R2]
BRZERO 0x0001
I-$
RF
LD R1, MEM[R0]
ADD R2, R2, #1
ADD R3, R2, #1
0x0001
0x0002
0x0003
0x0004
MUL R1, R2, R3
0x0005
0x0006
Flush!!
0x0007
0x0003
0x0004
0x0005
0x0006
0x0007
D-$
PC
DEC
WB

## Slide 15: Simplest: Always Guess NextPC = PC + 4
Always predict the next sequential instruction is the next instruction to be executed
This is a form of next fetch address prediction (and branch prediction)
How can you make this more effective?
Idea: Maximize the chances that the next sequential instruction is the next instruction to be executed
  Software: Lay out the control flow graph such that the “likely next instruction” is on the not-taken path of a branch
    Profile guided code positioning  Pettis & Hansen, PLDI 1990.
  Hardware: ??? (how can you do this in hardware…)
    Cache traces of executed instructions  Trace cache
Notes: Pettis and Hansen, Profile guided code positioning, PLDI 1990.
Trace caches…

## Slide 16: Guessing NextPC = PC + 4
How else can you make this more effective?
Idea: Get rid of control flow instructions (or minimize their occurrence)
How?
  1. Get rid of unnecessary control flow instructions  combine predicates (predicate combining)
  2. Convert control dependences into data dependences  predicated execution

## Slide 17: Branch Prediction: Always PC+4
IFPC
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
IFPC+4
IFPC
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
ID
IFPC+8
Insth branch condition and target
evaluated in ALU
IFPC+4
IFPC
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
ID
IFPC+8
ALU
ID
IFtarget
MEM
When a branch resolves
- branch target (Instk) is fetched
- all instructions fetched since
insth (so called “wrong-path”
instructions) must be flushed
Insth is a branch

## Slide 18: Pipeline Flush on a Misprediction
IFPC+4
IFPC
t0
t1
t2
t3
t4
t5
Insti
Instj
Instk
Instl
Insth
ID
ALU
ID
IFPC+8
IFtarget
MEM
ID
IF
WB
killed
killed
ALU
ID
IF
ALU
ID
IF
WB
Insth is a branch

## Slide 19: Performance Analysis
correct guess  no penalty ~86% of the time
incorrect guess  2 bubbles
Assume
  no data dependency related stalls
  20% control flow instructions
  70% of control flow instructions are taken
  CPI = [ 1 + (0.20*0.7) * 2 ] =
  = [ 1 + 0.14 * 2 ] = 1.28
penalty for
a wrong guess
probability of
a wrong guess
Can we reduce either of the two penalty terms?

## Slide 20: Reducing Branch Misprediction Penalty
Resolve branch condition and target address early
  CPI = [ 1 + (0.2*0.7) * 1 ] = 1.14
[Based on original figure from P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]
Is this a good idea?

## Slide 21: Branch Prediction (A Bit More Enhanced)
Idea: Predict the next fetch address (to be used in the next cycle)
Requires three things to be predicted at fetch stage:
  Whether the fetched instruction is a branch
  (Conditional) branch direction
  Branch target address (if taken)
Observation: Target address remains the same for a conditional direct branch across dynamic instances
  Idea: Store the target address from previous instance and access it with the PC
  Called Branch Target Buffer (BTB) or Branch Target Address Cache

## Slide 22: Fetch Stage with BTB and Direction Prediction
target address
Direction predictor (taken?)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + inst size
taken?
Next Fetch
Address
hit?
Address of the
current branch

## Slide 23: More Sophisticated Branch Direction Prediction
target address
Direction predictor (taken?)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
Global branch
history
XOR
PC + inst size
taken?
Next Fetch
Address
hit?
Which direction earlier
branches went
Address of the
current branch

## Slide 24: Three Things to Be Predicted
Requires three things to be predicted at fetch stage:
  1. Whether the fetched instruction is a branch
  2. (Conditional) branch direction
  3. Branch target address (if taken)
Third (3.) can be accomplished using a BTB
  Remember target address computed last time branch was executed
First (1.) can be accomplished using a BTB
  If BTB provides a target address for the program counter, then it must be a branch
  Or, we can store “branch metadata” bits in instruction cache/memory  partially decoded instruction stored in I-cache
Second (2.): How do we predict the direction?

## Slide 25: Simple Branch Direction Prediction Schemes
Compile time (static)
  Always not taken
  Always taken
  BTFN (Backward taken, forward not taken)
  Profile based (likely direction)
Run time (dynamic)
  Last time prediction (single-bit)

## Slide 26: More Sophisticated Direction Prediction
Compile time (static)
  Always not taken
  Always taken
  BTFN (Backward taken, forward not taken)
  Profile based (likely direction)
  Program analysis based (likely direction)
Run time (dynamic)
  Last time prediction (single-bit)
  Two-bit counter based prediction
  Two-level prediction (global vs. local)
  Hybrid
  Advanced algorithms (e.g., using perceptrons)

## Slide 27: Static Branch Prediction (I)
Always not-taken
  Simple to implement: no need for BTB, no direction prediction
  Low accuracy: ~30-40% (for conditional branches)
  Remember: Compiler can layout code such that the likely path is the “not-taken” path  more effective prediction
Always taken
  No direction prediction
  Better accuracy: ~60-70% (for conditional branches)
    Backward branches (i.e. loop branches) are usually taken
    Backward branch: target address lower than branch PC
Backward taken, forward not taken (BTFN)
  Predict backward (loop) branches as taken, others not-taken

## Slide 28: Static Branch Prediction (II)
Profile-based
  Idea: Compiler determines likely direction for each branch using a profile run. Encodes that direction as a hint bit in the branch instruction format.
+ Per branch prediction (more accurate than schemes in previous slide)  accurate if profile is representative!
-- Requires hint bits in the branch instruction format
-- Accuracy depends on dynamic branch behavior:
TTTTTTTTTTNNNNNNNNNN  50% accuracy TNTNTNTNTNTNTNTNTNTN  50% accuracy
-- Accuracy depends on the representativeness of profile input set

## Slide 29: Static Branch Prediction (III)
Program-based (or, program analysis based)
  Idea: Use heuristics based on program analysis to determine statically-predicted direction
  Example opcode heuristic: Predict BLEZ as NT (negative integers used as error values in many programs)
  Example loop heuristic: Predict a branch guarding a loop execution as taken (i.e., execute the loop)
  Pointer and FP comparisons: Predict not equal
+ Does not require profiling
-- Heuristics might be not representative or good
-- Requires compiler analysis and ISA support (ditto for other static methods)
Ball and Larus, ”Branch prediction for free,” PLDI 1993.
  20% misprediction rate

## Slide 30: Static Branch Prediction (IV)
Programmer-based
  Idea: Programmer provides the statically-predicted direction
  Via pragmas in the programming language that qualify a branch as likely-taken versus likely-not-taken
+ Does not require profiling or program analysis
+ Programmer may know some branches and their program better than other analysis techniques
-- Requires programming language, compiler, ISA support
-- Burdens the programmer?

## Slide 31: Pragmas
Idea: Keywords that enable a programmer to convey hints to lower levels of the transformation hierarchy
if (likely(x)) { ... }
if (unlikely(error)) { … }
Many other hints and optimizations can be enabled with pragmas
  E.g., whether a loop can be parallelized
  #pragma omp parallel
  Description
    The omp parallel directive explicitly instructs the compiler to parallelize the chosen segment of code.

## Slide 32: Static Branch Prediction
All previous techniques can be combined
  Profile based
  Program based
  Programmer based
How would you do that?
What is the common disadvantage of all three techniques?
  Cannot adapt to dynamic changes in branch behavior
    This can be mitigated by a dynamic compiler, but not at a fine granularity (and a dynamic compiler has its overheads…)
    What is a Dynamic Compiler?
      A compiler that generates code at runtime
      Java JIT (just in time) compiler, Microsoft CLR (common lang. runtime)

## Slide 33: More Sophisticated Direction Prediction
Compile time (static)
  Always not taken
  Always taken
  BTFN (Backward taken, forward not taken)
  Profile based (likely direction)
  Program analysis based (likely direction)
Run time (dynamic)
  Last time prediction (single-bit)
  Two-bit counter based prediction
  Two-level prediction (global vs. local)
  Hybrid
  Advanced algorithms (e.g., using perceptrons)

## Slide 34: Dynamic Branch Prediction
Idea: Predict branches based on dynamic information (collected at run-time)
Advantages
  + Prediction based on history of the execution of branches
  + It can adapt to dynamic changes in branch behavior
  + No need for static profiling: input set representativeness problem goes away
Disadvantages
  -- More complex (requires additional hardware)

## Slide 35: Last Time Predictor
Last time predictor
  Single bit per branch (stored in BTB)
  Indicates which direction branch went last time it executed
  TTTTTTTTTTNNNNNNNNNN  90% accuracy
Always mispredicts the last iteration and the first iteration of a loop branch
  Accuracy for a loop with N iterations = (N-2)/N
+ Loop branches for loops with large N (number of iterations)
-- Loop branches for loops will small N (number of iterations)
TNTNTNTNTNTNTNTNTNTN  0% accuracy

## Slide 36: Design of Digital Circuits Lecture 17b: Branch Prediction I
Prof. Onur Mutlu
ETH Zurich
Spring 2019
18 April 2019

## Slide 37: We did not cover the following slides. They are for your preparation for the next lecture.

## Slide 38: Implementing the Last-Time Predictor
BTB: one target
address per entry
BTB index
N-bit
tag
table
1 0
PC+4
nextPC
=
The 1-bit BHT (Branch History Table) entry is updated with the correct outcome after each execution of a branch
tag
BHT:
One
Bit
per
entry
taken?

## Slide 39: State Machine for Last-Time Prediction
predict
taken
predict
not
taken
actually
not taken
actually
taken
actually
taken
actually
not taken

## Slide 40: Improving the Last Time Predictor
Problem: A last-time predictor changes its prediction from TNT or NTT too quickly
  even though the branch may be mostly taken or mostly not taken
Solution Idea: Add hysteresis to the predictor so that prediction does not change on a single different outcome
  Use two bits to track the history of predictions for a branch instead of a single bit
  Can have 2 states for T or NT instead of 1 state for each
Smith, “A Study of Branch Prediction Strategies,” ISCA 1981.

## Slide 41: Two-Bit Counter Based Prediction
Each branch associated with a two-bit counter
One more bit provides hysteresis
A strong prediction does not change with one single different outcome
  Accuracy for a loop with N iterations = (N-1)/N
  TNTNTNTNTNTNTNTNTNTN  50% accuracy
  (assuming counter initialized to weakly taken)
  + Better prediction accuracy
  -- More hardware cost (but counter can be part of a BTB entry)

## Slide 42: State Machine for 2-bit Saturating Counter
Counter using saturating arithmetic
  Arithmetic with maximum and minimum values
pred
taken
11
pred
taken
10
pred
!taken
01
pred
!taken
00
actually
taken
actually
taken
actually
!taken
actually
!taken
actually
!taken
actually
!taken
actually
taken
actually
taken

## Slide 43: Hysteresis Using a 2-bit Counter
pred
taken
pred
taken
pred
!taken
pred
!taken
actually
taken
actually
taken
actually
!taken
actually
!taken
actually
!taken
actually
!taken
actually
taken
actually
taken
Change prediction after 2 consecutive mistakes
“weakly
taken”
“strongly
taken”
“weakly
!taken”
“strongly
!taken”

## Slide 44: Is This Good Enough?
~85-90% accuracy for many programs with 2-bit counter based prediction (also called bimodal prediction)
Is this good enough?
How big is the branch problem?

## Slide 45: Let’s Do the Exercise Again
Assume N = 20 (20 pipe stages), W = 5 (5 wide fetch)
  Assume: 1 out of 5 instructions is a branch
  Assume: Each 5 instruction-block ends with a branch
How long does it take to fetch 500 instructions?
  100% accuracy
    100 cycles (all instructions fetched on the correct path)
    No wasted work; IPC = 500/100
  90% accuracy
    100 (correct path) + 20 * 10 (wrong path) = 300 cycles
    200% extra instructions fetched; IPC = 500/300
  85% accuracy
    100 (correct path) + 20 * 15 (wrong path) = 400 cycles
    300% extra instructions fetched; IPC = 500/400
  80% accuracy
    100 (correct path) + 20 * 20 (wrong path) = 500 cycles
    400% extra instructions fetched; IPC = 500/500

## Slide 46: Can We Do Better: Two-Level Prediction
Last-time and 2BC predictors exploit “last-time” predictability
Realization 1: A branch’s outcome can be correlated with other branches’ outcomes
  Global branch correlation
Realization 2: A branch’s outcome can be correlated with past outcomes of the same branch (other than the outcome of the branch “last-time” it was executed)
  Local branch correlation
Yeh and Patt, “Two-Level Adaptive Training Branch Prediction,” MICRO 1991.

## Slide 47: Global Branch Correlation (I)
Recently executed branch outcomes in the execution path are correlated with the outcome of the next branch
If first branch not taken, second also not taken
If first branch taken, second definitely not taken

## Slide 48: Global Branch Correlation (II)
If Y and Z both taken, then X also taken
If Y or Z not taken, then X also not taken

## Slide 49: Global Branch Correlation (III)
Eqntott, SPEC’92: Generates truth table from Boolean expr.
  if (aa==2) ;; B1
  aa=0;
  if (bb==2) ;; B2
  bb=0;
  if (aa!=bb) { ;; B3
  ….
  }
  If B1 is not taken (i.e., aa==0@B3) and B2 is not taken (i.e. bb=0@B3) then B3 is certainly taken

## Slide 50: Capturing Global Branch Correlation
Idea: Associate branch outcomes with “global T/NT history” of all branches
Make a prediction based on the outcome of the branch the last time the same global branch history was encountered
Implementation:
  Keep track of the “global T/NT history” of all branches in a register  Global History Register (GHR)
  Use GHR to index into a table that recorded the outcome that was seen for each GHR value in the recent past  Pattern History Table (table of 2-bit counters)
Global history/branch predictor
Uses two levels of history (GHR + history at that GHR)
Yeh and Patt, “Two-Level Adaptive Training Branch Prediction,” MICRO 1991.

## Slide 51: Two Level Global Branch Prediction
First level: Global branch history register (N bits)
  The direction of last N branches
Second level: Table of saturating counters for each history entry
  The direction the branch took the last time the same history was seen
1 1 ….. 1 0
GHR
(global history register)
00 …. 00
00 …. 01
00 …. 10
11 …. 11
0
1
2
3
index
Pattern History Table (PHT)
previous
branch’s
direction
Yeh and Patt, “Two-Level Adaptive Training Branch Prediction,” MICRO 1991.

## Slide 52: How Does the Global Predictor Work?
McFarling, “Combining Branch Predictors,” DEC WRL TR 1993.
This branch tests i
Last 4 branches test j
History: TTTN
Predict taken for i
Next history: TTNT
(shift in last outcome)
Notes: Start with j=3, last iteration that is not taken…

## Slide 53: Intel Pentium Pro Branch Predictor
Two level global branch predictor
4-bit global history register
Multiple pattern history tables (of 2 bit counters)
  Which pattern history table to use is determined by lower order bits of the branch address

## Slide 54: Improving Global Predictor Accuracy
Idea: Add more context information to the global predictor to take into account which branch is being predicted
  Gshare predictor: GHR hashed with the Branch PC
  + More context information used for prediction
  + Better utilization of the two-bit counter array
  -- Increases access latency
McFarling, “Combining Branch Predictors,” DEC WRL Tech Report, 1993.

## Slide 55: Review: One-Level Branch Predictor
target address
Direction predictor (2-bit counters)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + inst size
taken?
Next Fetch
Address
hit?
Address of the
current instruction

## Slide 56: Two-Level Global History Branch Predictor
target address
Direction predictor (2-bit counters)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
Global branch
history
PC + inst size
taken?
Next Fetch
Address
hit?
Which direction earlier
branches went
Address of the
current instruction

## Slide 57: Two-Level Gshare Branch Predictor
target address
Direction predictor (2-bit counters)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
Global branch
history
XOR
PC + inst size
taken?
Next Fetch
Address
hit?
Which direction earlier
branches went
Address of the
current instruction

## Slide 58: Can We Do Better: Two-Level Prediction
Last-time and 2BC predictors exploit only “last-time” predictability for a given branch
Realization 1: A branch’s outcome can be correlated with other branches’ outcomes
  Global branch correlation
Realization 2: A branch’s outcome can be correlated with past outcomes of the same branch (in addition to the outcome of the branch “last-time” it was executed)
  Local branch correlation
Yeh and Patt, “Two-Level Adaptive Training Branch Prediction,” MICRO 1991.

## Slide 59: Local Branch Correlation
McFarling, “Combining Branch Predictors,” DEC WRL TR 1993.

## Slide 60: More Motivation for Local History
To predict a loop branch “perfectly”, we want to identify the last iteration of the loop
By having a separate PHT entry for each local history, we can distinguish different iterations of a loop
Works for “short” loops

## Slide 61: Capturing Local Branch Correlation
Idea: Have a per-branch history register
  Associate the predicted outcome of a branch with “T/NT history” of the same branch
Make a prediction based on the outcome of the branch the last time the same local branch history was encountered
Called the local history/branch predictor
Uses two levels of history (Per-branch history register + history at that history register value)

## Slide 62: Two Level Local Branch Prediction
First level: A set of local history registers (N bits each)
  Select the history register based on the PC of the branch
Second level: Table of saturating counters for each history entry
  The direction the branch took the last time the same history was seen
1 1 ….. 1 0
Local history registers
00 …. 00
00 …. 01
00 …. 10
11 …. 11
0
1
2
3
index
Pattern History Table (PHT)
Yeh and Patt, “Two-Level Adaptive Training Branch Prediction,” MICRO 1991.

## Slide 63: Two-Level Local History Branch Predictor
target address
Direction predictor (2-bit counters)
Cache of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + inst size
taken?
Next Fetch
Address
hit?
Address of the
current instruction
Which directions earlier instances of *this branch* went

## Slide 64: Can We Do Even Better?
Predictability of branches varies
Some branches are more predictable using local history
Some using global
For others, a simple two-bit counter is enough
Yet for others, a single bit is enough
Observation: There is heterogeneity in predictability behavior of branches
  No one-size fits all branch prediction algorithm for all branches
Idea: Exploit that heterogeneity by designing heterogeneous branch predictors

## Slide 65: Hybrid Branch Predictors
Idea: Use more than one type of predictor (i.e., multiple algorithms) and select the “best” prediction
  E.g., hybrid of 2-bit counters and global predictor
Advantages:
+ Better accuracy: different predictors are better for different branches
+ Reduced warmup time (faster-warmup predictor used until the slower-warmup predictor warms up)
Disadvantages:
-- Need “meta-predictor” or “selector”
-- Longer access latency
  McFarling, “Combining Branch Predictors,” DEC WRL Tech Report, 1993.

## Slide 66: Alpha 21264 Tournament Predictor
Minimum branch penalty: 7 cycles
Typical branch penalty: 11+ cycles
48K bits of target addresses stored in I-cache
Predictor tables are reset on a context switch
Kessler, “The Alpha 21264 Microprocessor,” IEEE Micro 1999.

## Slide 67: Are We Done w/ Branch Prediction?
Hybrid branch predictors work well
  E.g., 90-97% prediction accuracy on average
Some “difficult” workloads still suffer, though!
  E.g., gcc
  Max IPC with tournament prediction: 9
  Max IPC with perfect prediction: 35

## Slide 68: Some Other Branch Predictor Types
Loop branch detector and predictor
  Loop iteration count detector/predictor
  Works well for loops with small number of iterations, where iteration count is predictable
  Used in Intel Pentium M
Perceptron branch predictor
  Learns the direction correlations between individual branches
  Assigns weights to correlations
  Jimenez and Lin, “Dynamic Branch Prediction with Perceptrons,” HPCA 2001.
Hybrid history length based predictor
  Uses different tables with different history lengths
  Seznec, “Analysis of the O-Geometric History Length branch predictor,” ISCA 2005.

## Slide 69: Intel Pentium M Predictors
Gochman et al.,
“The Intel Pentium M Processor: Microarchitecture and Performance,”
Intel Technology Journal, May 2003.

## Slide 70: Perceptrons for Learning Linear Functions
A perceptron is a simplified model of a biological neuron
It is also a simple binary classifier
A perceptron maps an input vector X to a 0 or 1
  Input = Vector X
  Perceptron learns the linear function (if one exists) of how each element of the vector affects the output (stored in an internal Weight vector)
  Output = Weight.X + Bias > 0
In the branch prediction context
  Vector X: Branch history register bits
  Output: Prediction for the current branch

## Slide 71: Perceptron Branch Predictor (I)
Idea: Use a perceptron to learn the correlations between branch history register bits and branch outcome
A perceptron learns a target Boolean function of N inputs
  Jimenez and Lin, “Dynamic Branch Prediction with Perceptrons,” HPCA 2001.
  Rosenblatt, “Principles of Neurodynamics: Perceptrons and the Theory of Brain Mechanisms,” 1962
Each branch associated with a perceptron
A perceptron contains a set of weights wi
Each weight corresponds to a bit in
the GHR
How much the bit is correlated with the
direction of the branch
 Positive correlation: large + weight
 Negative correlation: large - weight
Prediction:
 Express GHR bits as 1 (T) and -1 (NT)
 Take dot product of GHR and weights
 If output > 0, predict taken

## Slide 72: Perceptron Branch Predictor (II)
Bias weight
(bias of branch, independent of
the history)
Dot product of GHR
and perceptron weights
Output
compared
to 0
Prediction function:
Training function:

## Slide 73: Perceptron Branch Predictor (III)
Advantages
  + More sophisticated learning mechanism  better accuracy
Disadvantages
  -- Hard to implement (adder tree to compute perceptron output)
  -- Can learn only linearly-separable functions
  e.g., cannot learn XOR type of correlation between 2 history bits and branch outcome

## Slide 74: Prediction Using Multiple History Lengths
Observation: Different branches require different history lengths for better prediction accuracy
Idea: Have multiple PHTs indexed with GHRs with different history lengths and intelligently allocate PHT entries to different branches
Seznec and Michaud, “A case for (partially) tagged Geometric History Length
Branch Prediction,” JILP 2006.

## Slide 75: State of the Art in Branch Prediction
See the Branch Prediction Championship
  https://www.jilp.org/cbp2016/program.html
Andre Seznec,
“TAGE-SC-L branch predictors,”
CBP 2014.
Andre Seznec,
“TAGE-SC-L branch predictors
again,” CBP 2016.

## Slide 76: Branch Confidence Estimation
Idea: Estimate if the prediction is likely to be correct
  i.e., estimate how “confident” you are in the prediction
Why?
  Could be very useful in deciding how to speculate:
    What predictor/PHT to choose/use
    Whether to keep fetching on this path
    Whether to switch to some other way of handling the branch, e.g. dual-path execution (eager execution) or dynamic predication
    …
Jacobsen et al., “Assigning Confidence to Conditional Branch Predictions,” MICRO 1996.

## Slide 77: Other Ways of Handling Branches

## Slide 78: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions.
Potential solutions if the instruction is a control-flow instruction:
Stall the pipeline until we know the next fetch address
Guess the next fetch address (branch prediction)
Employ delayed branching (branch delay slot)
Do something else (fine-grained multithreading)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 79: Delayed Branching (I)
Change the semantics of a branch instruction
  Branch after N instructions
  Branch after N cycles
Idea: Delay the execution of a branch. N instructions (delay slots) that come after the branch are always executed regardless of branch direction.
Problem: How do you find instructions to fill the delay slots?
  Branch must be independent of delay slot instructions
Unconditional branch: Easier to find instructions to fill the delay slot
Conditional branch: Condition computation should not depend on instructions in delay slots  difficult to fill the delay slot

## Slide 80: Delayed Branching (II)
A
B
C
BC X
D
E
F
if
ex
A
A
B
B
C
C
BC
BC
G
X:
--
A
B
C
BC X
D
E
F
G
X:
if
ex
A
A
C
C
BC
BC
B
B
G
--
G
Normal code:
Timeline:
Delayed branch code:
Timeline:
6 cycles
5 cycles

## Slide 81: Fancy Delayed Branching (III)
Delayed branch with squashing
  In SPARC
  Semantics: If the branch falls through (i.e., it is not taken), the delay slot instruction is not executed
  Why could this help?
A
B
C
BC X
D
E
X:
Normal code:
Delayed branch code:
A
B
C
BC X
D
E
X:
NOP
Delayed branch w/ squashing:
A
B
C
BC X
D
E
X:
A

## Slide 82: Delayed Branching (IV)
Advantages:
+ Keeps the pipeline full with useful instructions in a simple way assuming
1. Number of delay slots == number of instructions to keep the pipeline full before the branch resolves
2. All delay slots can be filled with useful instructions
Disadvantages:
  -- Not easy to fill the delay slots (even with a 2-stage pipeline)
  1. Number of delay slots increases with pipeline depth, superscalar execution width
  2. Number of delay slots should be variable with variable latency operations. Why?
-- Ties ISA semantics to hardware implementation
-- SPARC, MIPS, HP-PA: 1 delay slot
-- What if pipeline implementation changes with the next design?

## Slide 83: An Aside: Filling the Delay Slot
within same
basic block
For correctness:
add a new instruction
to the not-taken path?
For correctness:
add a new instruction
to the taken path?
Safe?
reordering data
independent
(RAW, WAW,
WAR)
instructions
does not change
program semantics
[Based on original figure from P&H CO&D, COPYRIGHT 2004 Elsevier. ALL RIGHTS RESERVED.]

## Slide 84: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions.
Potential solutions if the instruction is a control-flow instruction:
Stall the pipeline until we know the next fetch address
Guess the next fetch address (branch prediction)
Employ delayed branching (branch delay slot)
Do something else (fine-grained multithreading)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 85: Predicate Combining (not Predicated Execution)
Complex predicates are converted into multiple branches
  if ((a == b) && (c < d) && (a > 5000)) { … }
    3 conditional branches
Problem: This increases the number of control dependencies
Idea: Combine predicate operations to feed a single branch instruction instead of having one branch for each
  Predicates stored and operated on using condition registers
  A single branch checks the value of the combined predicate
+ Fewer branches in code  fewer mipredictions/stalls
-- Possibly unnecessary work
-- If the first predicate is false, no need to compute other predicates
Condition registers exist in IBM RS6000 and the POWER architecture

## Slide 86: Predication (Predicated Execution)
Idea: Convert control dependence to data dependence
Simple example: Suppose we had a Conditional Move instruction…
  CMOV condition, R1  R2
  R1 = (condition == true) ? R2 : R1
  Employed in most modern ISAs (x86, Alpha)
Code example with branches vs. CMOVs
  if (a == 5) {b = 4;} else {b = 3;}
  CMPEQ condition, a, 5;
  CMOV condition, b  4;
  CMOV !condition, b  3;

## Slide 87: Predication (Predicated Execution)
D
D
Idea: Compiler converts control dependence into data dependence  branch is eliminated
  Each instruction has a predicate bit set based on the predicate computation
  Only instructions with TRUE predicates are committed (others turned into NOPs)
(normal branch code)
C
B
D
A
T
N
p1 = (cond)
branch p1, TARGET
mov b, 1
jmp JOIN
TARGET:
mov b, 0
A
B
C
B
C
D
A
(predicated code)
A
B
C
if (cond) {
b = 0;
}
else {
b = 1;
}
p1 = (cond)
(!p1) mov b, 1
(p1) mov b, 0
add x, b, 1
add x, b, 1

## Slide 88: Predicated Execution References
Allen et al., “Conversion of control dependence to data dependence,” POPL 1983.
Kim et al., “Wish Branches: Combining Conditional Branching and Predication for Adaptive Predicated Execution,” MICRO 2005.

## Slide 89: Conditional Move Operations
Very limited form of predicated execution
CMOV R1  R2
  R1 = (ConditionCode == true) ? R2 : R1
  Employed in most modern ISAs (x86, Alpha)

## Slide 90: Predicated Execution (II)
Predicated execution can be high performance and energy-efficient
Fetch Decode Rename Schedule RegisterRead Execute
A
B
C
D
A
E
F
Predicated Execution
Branch Prediction
Pipeline flush!!
E
D
B
F
nop
Fetch Decode Rename Schedule RegisterRead Execute
A
B
A
C
B
A
C
B
D
A
D
C
B
E
A
E
D
C
F
B
A
F
E
D
C
B
A
A
F
B
C
D
E
F
E
D
A
B
C
F
E
A
B
C
D
F
E
D
C
B
A
F
E
D
C
A
B
E
D
C
B
A
F
A
F
B
C
D
E

## Slide 91: Predicated Execution
Eliminates branches  enables straight line code (i.e., larger basic blocks in code)
Advantages
  Eliminates hard-to-predict branches
  Always-not-taken prediction works better (no branches)
  Compiler has more freedom to optimize code (no branches)
    control flow does not hinder inst. reordering optimizations
    code optimizations hindered only by data dependencies
Disadvantages
  Useless work: some instructions fetched/executed but discarded (especially bad for easy-to-predict branches)
  Requires additional ISA (and hardware) support
  Can we eliminate all branches this way?

## Slide 92: Predicated Execution vs. Branch Prediction
+ Eliminates mispredictions for hard-to-predict branches
+ No need for branch prediction for some branches
+ Good if misprediction cost > useless work due to predication
-- Causes useless work for branches that are easy to predict
-- Reduces performance if misprediction cost < useless work
-- Adaptivity: Static predication is not adaptive to run-time branch behavior. Branch behavior changes based on input set, program phase, control-flow path.

## Slide 93: Predicated Execution in Intel Itanium
Each instruction can be separately predicated
64 one-bit predicate registers
each instruction carries a 6-bit predicate field
An instruction is effectively a NOP if its predicate is false
cmp
br
else1
else2
br
then1
then2
join1
join2
p1 p2 cmp
join1
join2
else1
p2
then2
p1
else2
p2
then1
p1

## Slide 94: Conditional Execution in the ARM ISA
Almost all ARM instructions can include an optional condition code.
  Prior to ARM v8
An instruction with a condition code is executed only if the condition code flags in the CPSR meet the specified condition.

## Slide 95: Conditional Execution in ARM ISA

## Slide 96: Conditional Execution in ARM ISA

## Slide 97: Conditional Execution in ARM ISA

## Slide 98: Conditional Execution in ARM ISA

## Slide 99: Conditional Execution in ARM ISA

## Slide 100: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions.
Potential solutions if the instruction is a control-flow instruction:
Stall the pipeline until we know the next fetch address
Guess the next fetch address (branch prediction)
Employ delayed branching (branch delay slot)
Do something else (fine-grained multithreading)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 101: Multi-Path Execution
Idea: Execute both paths after a conditional branch
  For all branches: Riseman and Foster, “The inhibition of potential parallelism by conditional jumps,” IEEE Transactions on Computers, 1972.
  For a hard-to-predict branch: Use dynamic confidence estimation
Advantages:
  + Improves performance if misprediction cost > useless work
  + No ISA change needed
Disadvantages:
  -- What happens when the machine encounters another hard-to-predict branch? Execute both paths again?
  -- Paths followed quickly become exponential
  -- Each followed path requires its own context (registers, PC, GHR)
  -- Wasted work (and reduced performance) if paths merge

## Slide 102: Dual-Path Execution versus Predication
Hard to predict
C
D
E
F
B
D
E
F
A
B
C
D
E
F
path 1
path 2
C
D
E
F
B
path 1
path 2
Dual-path
Predicated Execution
CFMerge
CFMerge

## Slide 103: Handling Other Types of Branches

## Slide 104: Remember: Branch Types
Type | Direction at fetch time | Number of possible next fetch addresses? | When is next fetch address resolved?
Conditional | Unknown | 2 | Execution (register dependent)
Unconditional | Always taken | 1 | Decode (PC + offset)
Call | Always taken | 1 | Decode (PC + offset)
Return | Always taken | Many | Execution (register dependent)
Indirect | Always taken | Many | Execution (register dependent)
How can we predict an indirect branch with many target addresses?

## Slide 105: Call and Return Prediction
Direct calls are easy to predict
  Always taken, single target
  Call marked in BTB, target predicted by BTB
Returns are indirect branches
  A function can be called from many points in code
  A return instruction can have many target addresses
    Next instruction after each call point for the same function
  Observation: Usually a return matches a call
  Idea: Use a stack to predict return addresses (Return Address Stack)
    A fetched call: pushes the return (next instruction) address on the stack
    A fetched return: pops the stack and uses the address as its predicted target
    Accurate most of the time: 8-entry stack  > 95% accuracy
Call X
…
  Call X
  …
    Call X
    …
    Return
  Return
Return

## Slide 106: Indirect Branch Prediction (I)
Register-indirect branches have multiple targets
Used to implement
  Switch-case statements
  Virtual function calls
  Jump tables (of function pointers)
  Interface calls
TARG
A+1
A
T
N
a
b
A
d
?
Conditional (Direct) Branch
Indirect Jump
r
br.cond TARGET
R1 = MEM[R2]
branch R1

## Slide 107: Indirect Branch Prediction (II)
No direction prediction needed
Idea 1: Predict the last resolved target as the next fetch address
  + Simple: Use the BTB to store the target address
  -- Inaccurate: 50% accuracy (empirical). Many indirect branches switch between different targets
Idea 2: Use history based target prediction
  E.g., Index the BTB with GHR XORed with Indirect Branch PC
  Chang et al., “Target Prediction for Indirect Jumps,” ISCA 1997.
  + More accurate
  -- An indirect branch maps to (too) many entries in BTB
  -- Conflict misses with other branches (direct or indirect)
  -- Inefficient use of space if branch has few target addresses

## Slide 108: Intel Pentium M Indirect Branch Predictor
Gochman et al.,
“The Intel Pentium M Processor: Microarchitecture and Performance,”
Intel Technology Journal, May 2003.

## Slide 109: Issues in Branch Prediction (I)
Need to identify a branch before it is fetched
How do we do this?
  BTB hit  indicates that the fetched instruction is a branch
  BTB entry contains the “type” of the branch
  Pre-decoded “branch type” information stored in the instruction cache identifies type of branch
What if no BTB?
  Bubble in the pipeline until target address is computed
  E.g., IBM POWER4

## Slide 110: Latency of Branch Prediction
Latency: Prediction is latency critical
  Need to generate next fetch address for the next cycle
  Bigger, more complex predictors are more accurate but slower
PC + inst size
Next Fetch
Address
BTB target
Return Address Stack target
Indirect Branch Predictor target
Resolved target from Backend
???

## Slide 111: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 112: VLIW

## Slide 113: VLIW Concept
Superscalar
  Hardware fetches multiple instructions and checks dependencies between them
VLIW (Very Long Instruction Word)
  Software (compiler) packs independent instructions in a larger “instruction bundle” to be fetched and executed concurrently
  Hardware fetches and executes the instructions in the bundle concurrently
No need for hardware dependency checking between concurrently-fetched instructions in the VLIW model

## Slide 114: VLIW Concept
Fisher, “Very Long Instruction Word architectures and the ELI-512,” ISCA 1983.
  ELI: Enormously longword instructions (512 bits)

## Slide 115: VLIW (Very Long Instruction Word)
A very long instruction word consists of multiple independent instructions packed together by the compiler
  Packed instructions can be logically unrelated (contrast with SIMD/vector processors, which we will see soon)
Idea: Compiler finds independent instructions and statically schedules (i.e. packs/bundles) them into a single VLIW instruction
Traditional Characteristics
  Multiple functional units
  All instructions in a bundle are executed in lock step
  Instructions in a bundle statically aligned to be directly fed into the functional units

## Slide 116: VLIW Performance Example (2-wide bundles)
lw $t0, 40($s0)
add $t1, $s1, $s2
sub $t2, $s1, $s3 and $t3, $s3, $s4 or $t4, $s1, $s5
sw $s5, 80($s0)
Ideal IPC = 2
Actual IPC = 2 (6 instructions issued in 3 cycles)

## Slide 117: VLIW Lock-Step Execution
Lock-step (all or none) execution: If any operation in a VLIW instruction stalls, all instructions stall
In a truly VLIW machine, the compiler handles all dependency-related stalls, hardware does not perform dependency checking
  What about variable latency operations?

## Slide 118: VLIW Philosophy
Philosophy similar to RISC (simple instructions and hardware)
  Except multiple instructions in parallel
RISC (John Cocke, 1970s, IBM 801 minicomputer)
  Compiler does the hard work to translate high-level language code to simple instructions (John Cocke: control signals)
    And, to reorder simple instructions for high performance
  Hardware does little translation/decoding  very simple
VLIW (Josh Fisher, ISCA 1983)
  Compiler does the hard work to find instruction level parallelism
  Hardware stays as simple and streamlined as possible
    Executes each instruction in a bundle in lock step
    Simple  higher frequency, easier to design

## Slide 119: Commercial VLIW Machines
Multiflow TRACE, Josh Fisher (7-wide, 28-wide)
Cydrome Cydra 5, Bob Rau
Transmeta Crusoe: x86 binary-translated into internal VLIW
TI C6000, Trimedia, STMicro (DSP & embedded processors)
  Most successful commercially
Intel IA-64
  Not fully VLIW, but based on VLIW principles
  EPIC (Explicitly Parallel Instruction Computing)
  Instruction bundles can have dependent instructions
  A few bits in the instruction format specify explicitly which instructions in the bundle are dependent on which other ones

## Slide 120: VLIW Tradeoffs
Advantages
  + No need for dynamic scheduling hardware  simple hardware
  + No need for dependency checking within a VLIW instruction  simple hardware for multiple instruction issue + no renaming
  + No need for instruction alignment/distribution after fetch to different functional units  simple hardware
Disadvantages
  -- Compiler needs to find N independent operations per cycle
  -- If it cannot, inserts NOPs in a VLIW instruction
  -- Parallelism loss AND code size increase
  -- Recompilation required when execution width (N), instruction latencies, functional units change (Unlike superscalar processing)
  -- Lockstep execution causes independent operations to stall
  -- No instruction can progress until the longest-latency instruction completes

## Slide 121: VLIW Summary
VLIW simplifies hardware, but requires complex compiler techniques
Solely-compiler approach of VLIW has several downsides that reduce performance
  -- Too many NOPs (not enough parallelism discovered)
  -- Static schedule intimately tied to microarchitecture
  -- Code optimized for one generation performs poorly for next
  -- No tolerance for variable or long-latency operations (lock step)
++ Most compiler optimizations developed for VLIW employed in optimizing compilers (for superscalar compilation)
  Enable code optimizations
++ VLIW successful when parallelism is easier to find by the compiler (traditionally embedded markets, DSPs)

## Slide 122: An Example Work: Superblock
Lecture Video on Static Instruction Scheduling
  https://www.youtube.com/watch?v=isBEVkIjgGA
Hwu et al., The superblock: An effective technique for VLIW and superscalar compilation.
The Journal of Supercomputing, 1993.

## Slide 123: Another Example Work: IMPACT
Chang et al., IMPACT: an architectural framework for multiple-instruction-issue processors. ISCA 1991.

## Slide 124: Approaches to (Instruction-Level) Concurrency
Pipelining
Out-of-order execution
Dataflow (at the ISA level)
Superscalar Execution
VLIW
Fine-Grained Multithreading
SIMD Processing (Vector and array processors, GPUs)
Decoupled Access Execute
Systolic Arrays

## Slide 125: Recall: How to Handle Data Dependences
Anti and output dependences are easier to handle
  write to the destination in one stage and in program order
Flow dependences are more interesting
Five fundamental ways of handling flow dependences
  Detect and wait until value is available in register file
  Detect and forward/bypass data to dependent instruction
  Detect and eliminate the dependence at the software level
    No need for the hardware to detect dependence
  Predict the needed value(s), execute “speculatively”, and verify
  Do something else (fine-grained multithreading)
    No need to detect

## Slide 126: How to Handle Control Dependences
Critical to keep the pipeline full with correct sequence of dynamic instructions.
Potential solutions if the instruction is a control-flow instruction:
Stall the pipeline until we know the next fetch address
Guess the next fetch address (branch prediction)
Employ delayed branching (branch delay slot)
Do something else (fine-grained multithreading)
Eliminate control-flow instructions (predicated execution)
Fetch from both possible paths (if you know the addresses of both possible paths) (multipath execution)

## Slide 127: Fine-Grained Multithreading

## Slide 128: Fine-Grained Multithreading
Idea: Hardware has multiple thread contexts (PC+registers). Each cycle, fetch engine fetches from a different thread.
  By the time the fetched branch/instruction resolves, no instruction is fetched from the same thread
  Branch/instruction resolution latency overlapped with execution of other threads’ instructions
+ No logic needed for handling control and
data dependences within a thread
-- Single thread performance suffers
-- Extra logic for keeping thread contexts
-- Does not overlap latency if not enough
threads to cover the whole pipeline
Notes: Latency overlap/hiding

## Slide 129: Fine-Grained Multithreading (II)
Idea: Switch to another thread every cycle such that no two instructions from a thread are in the pipeline concurrently
Tolerates the control and data dependency latencies by overlapping the latency with useful work from other threads
Improves pipeline utilization by taking advantage of multiple threads
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.

## Slide 130: Fine-Grained Multithreading: History
CDC 6600’s peripheral processing unit is fine-grained multithreaded
  Thornton, “Parallel Operation in the Control Data 6600,” AFIPS 1964.
  Processor executes a different I/O thread every cycle
  An operation from the same thread is executed every 10 cycles
Denelcor HEP (Heterogeneous Element Processor)
  Smith, “A pipelined, shared resource MIMD computer,” ICPP 1978.
  120 threads/processor
  available queue vs. unavailable (waiting) queue for threads
  each thread can have only 1 instruction in the processor pipeline; each thread independent
  to each thread, processor looks like a non-pipelined machine
  system throughput vs. single thread performance tradeoff

## Slide 131: Fine-Grained Multithreading in HEP
Cycle time: 100ns
8 stages  800 ns to complete an instruction
  assuming no memory access
No control and data dependency checking
Burton Smith
(1941-2018)

## Slide 132: Multithreaded Pipeline Example
Slide credit: Joel Emer

## Slide 133: Sun Niagara Multithreaded Pipeline
Kongetira et al., “Niagara: A 32-Way Multithreaded Sparc Processor,” IEEE Micro 2005.

## Slide 134: Fine-grained Multithreading
Advantages
  + No need for dependency checking between instructions
  (only one instruction in pipeline from a single thread)
  + No need for branch prediction logic
  + Otherwise-bubble cycles used for executing useful instructions from different threads
  + Improved system throughput, latency tolerance, utilization
Disadvantages
  - Extra hardware complexity: multiple hardware contexts (PCs, register files, …), thread selection logic
  - Reduced single thread performance (one instruction fetched every N cycles from the same thread)
  - Resource contention between threads in caches and memory
  - Some dependency checking logic between threads remains (load/store)

## Slide 135: Modern GPUs are FGMT Machines

## Slide 136: NVIDIA GeForce GTX 285 “core”
…
= instruction stream decode
= data-parallel (SIMD) func. unit,
control shared across 8 units
= execution context storage
= multiply-add
= multiply
64 KB of storage
for thread contexts (registers)
Slide credit: Kayvon Fatahalian
Notes: 30 * 32 * 32 = 30 * 1024 = 30K fragments
64KB register file = 16 32-bit registers per thread = 64B (1/32 that of LRB)
16KB of shared scratch
80KB / core available to software

## Slide 137: NVIDIA GeForce GTX 285 “core”
…
64 KB of storage
for thread contexts (registers)
Groups of 32 threads share instruction stream (each group is a Warp): they execute the same instruction on different data
Up to 32 warps are interleaved in an FGMT manner
Up to 1024 thread contexts can be stored
Slide credit: Kayvon Fatahalian
Notes: To get maximal latency hiding:
Run 1/32 of the time
16 words per thread = 64B

## Slide 138: NVIDIA GeForce GTX 285
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
Tex
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
30 cores on the GTX 285: 30,720 threads
Slide credit: Kayvon Fatahalian
Notes: If you’re running a CUDA program, and your not launching 30K threads, you are certainly not getting full latency hiding, and you might not be using the GPU well

## Slide 139: End of Fine-Grained Multithreading